## Slide 1: Current development towards wide bandwidth front-ends for VLBI
Miroslav Pantaleev, Leif Helldner, Ulf Kylenfall,
Lars Pettersson, Per Björklund

## Slide 2: Outline
Motivation and challanges
DIVA project
C-band front-end for OSO 25m
C/X band front-end study for OSO 20m
Beyond 3:1
Summary
Questions

## Slide 3: Motivation and Challanges
Extend the IF band width
Provide back-up solution for existing systems at other telescopes to minimise the down time
Find solution at existing telescope with complicated already existing RF system
Keep the development and implantation cost low
Minimise the down time

## Slide 4: DIVA project
Study Wide-Band systems for VLBI and SKA in order to create the possibility of significantly larger instantaneous bandwidth of observations
Explore new technologies for the Low Noise Amplifiers (LNA): 70nm mHEMTs from OMMIC and 50nm mHEMTs from IAF (Fraunhofer).
Research, design and evaluation will focus on low power, wide bandwidth and very low noise temperatures.
Integrate the LNAs with Wide-Band single pixel feeds to demonstrate the system performance.
J G Bij de Vaate, Roel Witvers, ASTRON
M Pantaleev, M Lindqvist, Onsala
R Keller, W Alef, MPG

## Slide 5: DIVA project
LNA development
ASTRON design (Roel Witvers)
Based on the Fraunhofer 50nm mHEMT
Single ended, two stage design with a cascode input stage.
The simulated s-parameters have a small signal gain of 35dB
The simulations show a NT <40K over the frequency band, the cryogenic noise temperature can be expected with an improvement factor of 7 to 10 compared the room temperature noise performance.
Ongoing work on differential LNA

## Slide 6: DIVA project
EVN Telescopes

## Slide 7: DIVA project
Feed – LNA integration
Onsala Observatory/Antenna Group at Chalmers
Use existing feed design and test with LNAs developed within the project
Investigate differential feeding
Develop concepts for large vacuum windows and IR filters
Integrate and measure Y-factor
Investigate the possibility for telescope tests.

## Slide 8: C-band front-end for OSO 25m
Extend the bandwidth of the C-band system based on septum polarizer
Purchased OMT from NRAO in September 2012
LNAs from GARD/Onsala Observatory
C-band system and L-band LNAs integrated in new common cryostat, installed on telescope in March 2012
~20K
Continuous coverage

## Slide 9: C-band front-end for OSO 25m

## Slide 10: C-band front-end for OSO 25m
Y-factor test done with C-band horn
Sky as cold load and absorber as ambient
Filters are used to limit the BW to 4.25-7GHz due to strong interferences
No corrections are done for losses in the horn or ground pick-up

## Slide 11: S/C/X-band front-end for OSO 20m
About 50 Geo-VLBI experiments per year
3 EVN sessions per year
Single dish observations mainly in the 3mm band
Integrate C-band receiver on 20m to increase the reliability for EVN
Minimize the changes in the receiver cabin
Keep compatibility with S/X band system
Improve Tsys
~20K
Continuous coverage 4-12GHZ

## Slide 12: Current layout 20m

## Slide 13: Current layout

## Slide 14: Feasibility study for 4 – 12.25 GHz front-end
Mark Bowen and Alex Dunnin
CSIRO Astronomy and Space Science
Smooth-walled spline-profile horn
Christophe Granet
BAE Systems Australia
Offset Quad Ridged Ortho-mode Transducer
Notes: Sample title slide
Copyright © 2005 BAE Systems. All rights reserved.

## Slide 15: Design of the 4 – 12.25 GHz Horn
BAE Systems Australia has been asked to perform a short feasibility study aimed at looking at the development of a 4 – 12.25 GHz feed system for the 20m-diameter antenna at the Onsala Space Observatory (OSO) in Sweden.
The antenna is used for radio astronomy research over the cm to mm wavelengths.
BAE Systems has developed and delivered two 4 – 12.25 GHz optimized horns to the CSIRO Astronomy and Space Science (CASS) for the Australia Telescope Compact Array (ATCA) 22m-diameter antenna.
The optimized horn is used in conjunction with the wideband OMT designed by CASS.

## Slide 16: Design of the 4 – 12.25 GHz Horn
The aim of the feasibility study is to design a new 4 – 12.25 GHz horn for the OSO 20m-diameter antenna that would also use the CASS OMT.
CASS will supply the OMT and associated noise coupler, gap-guide and vacuum window that need to be connected to the horn.
The geometry of the OSO 20m-diameter antenna is very different from the ATCA 22m-diameter antenna and the main issue is the subtended angle to the subreflector.
The 4 – 12.25 GHz horn for the ATCA was designed to have a nominal Gaussian radiation pattern with a taper of -12 dB at 14º, where the half-subtended angle of the subreflector is 14º.
For the OSO, the half subtended angle is only 6.09º and to achieve an edge taper of -12dB at 6.09º, the new horn will need to have a radiation pattern with a much higher directivity.

## Slide 17: Design of the 4 – 12.25 GHz Horn
OSO has indicated that the preferred option would be to have a new 4 – 12.25 GHz feed system situated where the current X-band feed is located.
This brings mechanical constraints to the design of the 4 – 12.25 GHz feed system and these mechanical constraints may be overcome by designing the horn so that it can be used for both the X-band GeoVLBI operations and the wide-band 4 – 12.25 GHz operations.
To do so, the horn will be designed in sections, with at least one mechanical flange at a position of 816mm from the input of the horn and a diameter of no more than 366mm, thus the existing tertiary with dichroic can be used.
The overall length of the 4 – 12.25 GHz horn will be set to be 1800mm with an aperture diameter target of around 550mm.

## Slide 18: Design of the 4 – 12.25 GHz Horn
The 4 – 12.25 GHz horn is an optimized smooth-walled spline-profile horn and the current (as of 03/11/2014) best geometry is show below:
Full-Size Horn
Horn “split” at 816mm for VLBI operations

## Slide 19: Design of the 4 – 12.25 GHz

## Slide 20: Radiation Patterns 4-12GHz feed

## Slide 21
Radiation Patterns 4-12GHz feed

## Slide 22
Radiation Patterns 4-12GHz feed

## Slide 23
Radiation Patterns 4-12GHz feed

## Slide 25: Radiation Patterns 4-12GHz feed

## Slide 26: Split Geo-VLBI feed

## Slide 27: Split Geo-VLBI feed

## Slide 28: Feed - Reflector system simulations preliminary results

## Slide 29: The Offset Probe OMT Design
A 16-26GHz offset probe OMT
Transition from circular to quad ridged waveguide
Polarisation separating junction
Rear Transition from double ridged waveguide to coax
Notes: The offset probe OMT
  To avoid the problems associated with the co-located probe design we have separated the probes in a offset probe design.
  The image in the top right corner is of a narrowband offset probe OMT. These OMTs have been developed in the past however they have not been shown to exhibit the same frequency coverage as the co-located probe designs
  The OMT considered here was designed in three separate sections, an input transition from circular to quad ridged waveguide, a ortho-mode junction which removes the A polarisation via a coaxial probe and a rear transition from double ridged waveguide to coax.
  Because of the nature of quad ridged waveguide only in the input transition must multiple propagating mode be considered.

## Slide 30: Back to back OMT measurements
Multiple short waveguide sections
Trapped Mode resonances
OMT insertion loss
OMT cross polarisation and isolation
Slight ellipticity caused by mechanical misalignment

## Slide 31: Current layout

## Slide 32: Feed-receiver integration front view

## Slide 33: Feed-receiver integration – side view

## Slide 34: Tripple band (S/X/Ka) system for 20m

## Slide 35: Summary
L/C band front-end for OSO 25m was developed using available state of the art components from Chalmers and NRAO
Receiver nose at C-band is lower than 20K
1.6-5GHz feed-LNA cryogenic system for FP7/DIVA is under development
Study of 4-12GHz front-end for OSO 20m is ongoing
Preliminary feed design shows good efficiency
Preparation for front-end integration in the telescope cabin is ongoing
Initial design for triple band system is suggested

## Slide 36: Questions?