## Slide 1
Arpad Szomoru, JIVE
Technical Operations and R&D at JIVE

## Slide 2: Mark5, SUs, MarkIV correlator
Mark5, general
  New Linux kernel + newest SdK would break e-VLBI
  Has been investigated by Paul Boven
    Fixed by Conduant
  Still some minor issues with SdK9.4
  Finally upgrade to non-antique Linux version! (Wheezy)
Mark5B/C
  2 units permanently converted to B
  1 extra unit currently B+, 6 C units in place
  1 C unit on loan to Yebes
  1 C unit on loan to Torun for DBBC verification
MkIV Correlator
  Gone!
  Correlator boards sent to Hawaii

## Slide 3: Jive5AB
Jive5ab has taken over most operational VLBI in EVN
  No major show stoppers, mishaps
Much development ongoing

## Slide 4: e-status
Full 1024 Mbps available from most stations
  Ef, On, Nt, Mh, Hh, Tr, Ys using DBBCs operationally
  Mc doing tests
  Jb received DBBC
Channel dropping possible when needed (except Ar)
Ar still at 512 Mbps
Irbene: full EVN member in 2015?
Still attempting to bring e-Merlin back into array

## Slide 5: SFXC Correlator
Used for all EVN operations, both recorded and real-time:
  e-VLBI with 13 stations at 1024 Mbps
Coherent de-dispersion
Multiple phase centers in real time!
Primary beam shape determination:
  Beams from Ef, On, Bd, Sv, Ys
  Single map from Tr
  More needed!

## Slide 7: SFXC Hardware
40 nodes; 384 cores (Intel Xeon 5500/5600/E5-2600)
QDR Infiniband interconnect (32 Mbit/s)
8 nodes with 10 GbE (currently limited to 20 Gbit/s total)
13 stations @1Gbit/s real-time (with cross-polarisations)

## Slide 8: SFXC Correlator: phasing up the EVN
Phased array mode
Coherent summing of signals
Mult. phase center capability for phased array mode under development
Implementation at KVN

## Slide 9: UniBoard and beyond
UniBoard-based EVN correlator
  Can now accept data from Mark5, FlexBuff
  Interesting problems remain
  Two UniBoards at JIVE
    32 stations at 1 Gbps
    Or 16 at 2 / 8 at 4
  Project review took place in September
    Very positive feedback from panel
UniBoard2
  Prototype will use 20nm FPGA technology
  Some (or all?) production boards with 14nm (pin compatible)
  Main board, optimized for use as AA-low beam former
  Full mesh, Hybrid Memory Cubes and QSFP+ cages on break-out board
  Tender has been issued, manufacturer selected

## Slide 10
Arpad Szomoru, JIVE
Joint EVN – LBA observations

## Slide 11: Some history
32 hour real-time (near-) continuous e-VLBI demo
Involving telescopes in Australia, Japan, China, Europe, the Americas
At opening of IYA2009, Paris
Led to three-epoch observations by Giroletti et al.
Then, nothing (not known, not supported,….)

## Slide 12: Why bother?
NEXPReS has finished
For time being, no formal collaboration between JIVE + EVN and LBA, CSIRO, AARNET
New Zealand looking at refurbishing 32m telescope
  Obviously working together with Australians
  But how to get them involved in world-wide VLBI?
SKA looming on horizon, eating up radio astronomy
VLBI will remain important, considering what baseline design looks like
But have to showcase this importance
  Be global, connected, active, transparent
LBA already observes regularly with some EVN stations

## Slide 13: Science case (?)
Left: source at Dec 0 (RG001)
  17 hours in total
  Longest N-S and E-W baselines with different telescopes
Right: source at Dec -10 (now includes Ar)
  19 hours in total

## Slide 14: Science case (!)
SGRA*
High frequencies preferred, KVN perfect for this

## Slide 15: And now
Board approved collaboration
  In call for proposals
  Until now, one very good candidate, did not ask for joint observations though
  Not sufficiently known in community?

## Slide 16
Arpad Szomoru, JIVE
Towards 2 - 4 Gbps operations

## Slide 17: Status
Current Problems:
Recording media
Common LO setting
  DDC mode needed!
Lack of FS support
To do:
Test DDC mode
Find solution for FS
Buy FlexBuffs/Mark6
Test Jive5AB on Mark6
Aim for 2Gbps for now (VLBA, CDAS, R1002)