## Slide 1: International LOFAR
VLBI at 140 MHz (and below)
Adam Deller, Javier Moldon, the LOFAR Long Baseline Working Group & more
Harris, Moldon, Oonk, Deller et al., in prep
Notes: Javier has done the majority of the data reduction and analysis shown here

## Slide 2: Why low-frequency VLBI?
Resolution, resolution, resolution
For even moderately compact structure at low frequency, you need long baselines
0.7” corresponds to:
  3 km baselines @ 45 GHz (VLA C array)
  9 km baselines @ 15 GHz (VLA B array)
  27 km baselines @ 4.5 GHz (VLA A array)
  100 km baselines @ 1.4 GHz (E-MERLIN)
  1200 km baselines @ 120 MHz (Intl. LOFAR)

## Slide 3: International LOFAR

## Slide 4: International LOFAR now…
Basic info
Max baseline: 1200 km
Usefully independent stations: ~20
Point source sensitivity: 0.12 mJy/beam in 1 hour
Frequency range: 15-90 MHz, 110-240 MHz
Instantaneous bandwidth: 96 MHz
Primary FoV: 3+ degrees (frequency dependent)
Number of beams: many (bandwidth division)

## Slide 5: International LOFAR… and soon
Basic info
Max baseline: 1550 km
Usefully independent stations: ~25
Point source sensitivity: 0.1 mJy/beam in 1 hour
Frequency range: 15-90 MHz, 110-240 MHz
Instantaneous bandwidth: 96 MHz
Primary FoV: 3+ degrees (frequency dependent)
Number of beams: many (bandwidth division)

## Slide 6: Differences with traditional VLBI
Sensitivity is squeezed front and back:
  Sky noise is higher
  Calibrator sources are fainter (most compact sources are flat or inverted)
But we have a lot of collecting area, which helps to compensate:
  Single international station 2,000 m2, 800 Jy
  Combined core stations: 25,000 m2, 65 Jy

## Slide 7: Differences with traditional VLBI
The real killer is the ionosphere:
  delayiono  2
  At 1.4 GHz, you get delay ~ few ns
  At 0.14 GHz, you get delay ~ few 100 ns!
    And 2x greater at 120 MHz vs 170 MHz…

## Slide 8: Differences with traditional VLBI
LOFAR
cm VLBI
Phase
Frequency
Clock
Ionosphere
Total

## Slide 9: International LOFAR calibration
A series of “non-standard” (compared to short-baseline LOFAR) steps:
  Calibrate and phase up core stations into “super-station” (visibility summation, offline)
  Convert to circular polarisation (avoid problems with Faraday rotation)
  Aggregate bandwidth in relatively narrow subbands (2-3 MHz)
  Solve w/traditional VLBI tools (FRING, CALIB)

## Slide 10: Results 1: M82 (Varenius et. al.)
M82: Varenius et. al., A&A, submitted

## Slide 11: Results II: Jet acceleration
Harris, Moldon, Oonk, Deller et al., in prep

## Slide 12: Results III: Blazars
VLA @ 1.4 GHz
LOFAR @ 0.14 GHz
Moldon et al., from a test dataset with just 8 MHz bandwidth and 3 hours on source!
Notes: Want to note, all of these get quite close to the thermal noise (dynamic range >1000:1), with nothing more than FRING and CALIB.

## Slide 13: Ongoing developments
Calibrator surveys
  Calibration solutions can be extrapolated for 15-30’ (depends on ionospheric conditions)
  How many calibrators are there?
Pipelines
  Until ~November 2014 (i.e., now) long baseline calibration was PI’s responsibility
  Observatory pipeline now available (saves PI from dealing with 10+ TB datasets)
  What is the next step?

## Slide 14: LOFAR Snapshot Calibrator Survey
Observe sources with S150MHz > 100 mJy
16 subbands = 3 MHz / beam
30 beams / scan
4 minutes / scan
360 sources inspected per hour
Advantage: No uv shifting means simple/fast processing and smaller data volumes
Two 1 hr observations taken in late 2013

## Slide 15: LOFAR Snapshot Calibrator Survey
Moldon, Deller et al., A&A, accepted

## Slide 16: Snapshot Calibrator Results
Predicted LOFAR flux density (mJy)
Moldon, Deller et al., A&A, accepted

## Slide 17: Snapshot Calibrator Results
Moldon, Deller et al., A&A, accepted

## Slide 18: LOFAR Snapshot Calibrator Survey
86 “good” sources from 89 sq. deg. “effective” sky area:
So: density of good calibrators ~1 per sq. deg.
Moldon, Deller et al., A&A, accepted
Notes: As you can see – there is a lot of green. Green is good! So now I’m going to show the main results we’ve been able to extract so far. PRELIMINARY! The analysis shown here was finished yesterday!! Only time to focus on the important correlations, and the headline result (number of calibrators per square degree).

## Slide 19: LOBOS: The next step
All-sky (δ> 0) survey for LOFAR long-baseline calibrators, PI N. Jackson.
96 hours awarded in next observing cycle (everything above +28.5 degrees)
  Expect to find 10,000 – 15,000 calibrator sources

## Slide 20: Supercharged calibration
LOFAR
Phase
Frequency
Clock
Ionosphere
Total
The number of independent variables is actually quite small:
Non-dispersive delay (and time derivative)
Dispersive delay (and time derivative)
Faraday rotation (and time derivative)
Phase offset (and time derivative?)
Solution space is very spiky, but can we use existing delay-rate solutions to guide a true global fit? Subject of a highly rated grant proposal.

## Slide 21: Conclusions
International LOFAR offers sub-arcsecond imaging at metre wavelengths for the first time
It’s not that hard! Standard VLBI tools will get you a dynamic ranges >> 1000:1
Even better sensitivity and fidelity expected once true dispersive delay + dispersive delay rate solve is implemented