## Slide 1: VLBI Developments in Australia
Astronomy and space science
Chris Phillips| LBA Lead Scientist
11 November 2014

## Slide 2: LBA
Core LBA 5 stations
  Parkes 64m, ATCA 5x22m, Mopra 22m, Hobart 26m, Ceduna 30m, Hartebeesthoek (26m)
Plus many when available
  Tidbinbilla (70m,34m), Warkworth (12m), ASKAP (12m)
1.4-22 GHz
  Plus 7mm and 3mm (Mp, At, Tid 34m)
Observes ~3 weeks/year in 3-4 session plus “special” sessions and Radioastron support

## Slide 3: LBA Status
ATNF 20% annual budget cut
  Significant cuts to observatories already due to impact of ASKAP
Impact on all existing facilities
Astro and engineering research particularly affected
Tasso Tzioumis: Assistant Director – Engineering
Me × ½: LBA Lead Scientist
Curtin continue LBA correlation for next 12 months

## Slide 4: Parkes
Reduce staff on site
No onsite observing – Sydney or home institute
Restricted receiver changes
  Standard receivers 1.4 GHz multibeam and pulsar 10/50 cm.
  1 “VLBI” swap every 6 months
  2 high frequency receivers each time
Funding received for wideband 700 MHz to 4 GHz receiver
Ongoing testing of 8 Gbps XCube sampler

## Slide 5: ATCA
Reduced operational staff
No onsite observing – Sydney or home institute
Considering focus on large scale projects, unattended observing
No immediate impact on VLBI
Ongoing discussions on wideband voltage output
  Currently restricted to 2x64 MHz despite 2x2 GHz digital frontend
  Using ASKAP processing boards rather than change CABB firmware

## Slide 6: Mopra
CSIRO “ceasing funding” of Mopra
External groups considering taking over full operations
  May not include VLBI operations….

## Slide 7: NRN Network funding
Funding for 10 Gbps networks to Parkes,
ATCA and Mopra
10 Gbps “ring” between observatories and Sydney for production traffic
  Routed via 10 Gbps firewall in Canberra (shared with rest CSIRO)
10 Gbps dedicated “research” links from observatories to supercomputing facilities around Australia
“First Packet” end Q1 2015

## Slide 10: Galaxy
Part of Pawsey IVEC supercomputing facility
Central Science Processor for ASKAP
Also available for general Radioastronomy community
Cray XC30 system
  484 nodes of 2x 10-core Intel E5-2690V2 ‘Ivy Bridge’
  64 nodes of 2x8-core Intel Xeon E5-2690, with NVIDIA K20X ‘Kepler’ GPU
  200 TFLOPS
  low-latency Aries interconnect.
Initial porting of DIFX started

## Slide 11: ASKAP PAF VLBI
ASKAP currently being built in Western Australia
36x12m, each with 36 beam PAF
  188 element “checker board”
Currently testing 6 station beta array
ASKAP12 with 2nd generation PAFs Q4 2015
Demonstrated VLBI with a single formed beam
  Approach would scale to multiple beams, though is far from production ready
Image Credit Rob Millenaar

## Slide 12: ASKAP Digital processing
VLBI
Proprietary data links
No provision for voltage capture
Use “monitor port” to capture 1 second buffer
  Duty cycle 1 in 10
  16x1 MHz channels (dual pol)

## Slide 13: “Oversampled” filterbank
ASKAP produces 384 channels over 384 MHz bandwidth, with a 1 MHz channel spacing
Sampling rate of complex channels is 32/27 MHz
  1.185… MHz

## Slide 14: VLBI challenges
No VLBI format can cope with non-integral sampling rate
  Resample
Oversampled filterbank design means DC channel of (most) channels is not centered in the middle and changes from channel to channel
  Need to apply a phase rotation to data to undo this affect
  Need to be “very” careful with numerology to get the initial phase right
  “Raw” files to not start on a 1 second boundary

## Slide 15: Resampling
Initially use IPP resampling routines
  “Up-down” resampling plus low pass filter (Complex data with DC in center)
No fringes
  SNR (1/2 MHz bandwidth)
  Phase offset problem (unrelated to actual approach)

## Slide 16: FFT Resampling
Data is 16x 1.185 MHz
Forward 32x2 point FFT on individual channels
Keep inner 54 points (64*27/32)
Switch together to form 16 MHz single channel
Inverse 864 point FFT
Format as VDIF

## Slide 17
- 64 points -
- 54 points -

## Slide 20: 7mm/3mm VLBI
Tid 34m, Mopra, ATCA 7mm frontends
Mopra, ATCA 3mm frontends
Simultaneous 3/7mm ATCA/KVN fringe

## Slide 21: A Global multi-Chan mm-VLBI array
7,300km
7,900km
9,000km
September:
Simultaneous 7/3mm fringes
Completing installation of QO for Simultaneous
13/7&3mm VLBI
2,300km
August:
Simultaneous
VLBI with KVN
Observations with KVN by end of 2014
2016:
Tests with MK

## Slide 22: Optical Fibre Phase Transfer
Continued work on transfer of a radio frequency (RF) reference via shared optical networks
Bi-directional amplifiers required
  Need to split signal at each stage of amplification (typically 80-100 km)

## Slide 23: Narrabri – Mopra - Narrabri Transfer
Live traffic
VLBI

## Slide 24: Dual-Channel Radiotelescope Measurements on 18/02/2014
Antenna 5 vs Antenna 4, 77 m apart
Antenna 3 vs Antenna 4, ~1.x km apart
Antenna 3 operates in dual channel mode
Antenna signal is processed by
two independent digitizes
on separate timing references
Radio telescope at 8.4 GHz

## Slide 25: Thank you
Astronomy and Space Science
  Chris Phillips LBA Lead Scientist
    t +61 2 9372 4608
    e Chris.Phillips@csiro.au
    w www.atnf.csiro.au
Astronomy and SPACE SCIENCE