## Slide 1: VGOS GPU Based Software Correlator Design
Igor Surkis, Voytsekh Ken, Vladimir Mishin,
Nadezhda Mishina, Yana Kurdubova, Violet Shantyr, Vladimir Zimovsky
Institute of Applied Astronomy, RAS
St. Petersburg, Russia
Third International VLBI Technology Workshop 10 - 13 November 2014, Groningen/Dwingeloo, the Netherlands

## Slide 2: Introduction
Third International VLBI Technology Workshop 10 - 13 November 2014, Groningen/Dwingeloo, the Netherlands
Specifications
Main design ideas
Basic modules
HPC cluster
Topology
Station module
Correlation module
Benchmarks
First fringe
Future plans
Badary and Zelenchukskaya VGOS antennas of “Quasar” VLBI network

## Slide 3: Correlator Specification
Third International VLBI Technology Workshop 10 - 13 November 2014, Groningen/Dwingeloo, the Netherlands
Input data stream of up to 16 Gbps from each of up to 6 observatories:
  2-bit sampling
  4 frequency bands:
    2 polarizations, 512 MHz bandwidth
    1 polarization, 1024 MHz bandwidth
VDIF data format
Cross-spectra resolution of up to 4096 spectral channels
(near-real time)
Extracting 32 phase calibration tones (near-real time)

## Slide 4: Main Design Ideas
Third International VLBI Technology Workshop 10 - 13 November 2014, Groningen/Dwingeloo, the Netherlands
The new correlator is a FX software one
The basic principles comes from the correlator DiFX ideas
The main distinctive feature is using Graphical Processing Units (GPUs) for the most computations, because GPU is equipped with hundreds of computing cores, and mathematical algorithms can be parallelized – less processing units, less traffic between modules
Hardware is based on the hybrid blade servers (CPU+GPU) in the high-perfomance computing cluster

## Slide 5: Basic Modules
Third International VLBI Technology Workshop 10 - 13 November 2014, Groningen/Dwingeloo, the Netherlands
Spectus 2U cache server / V200F CM:
station module / correlation module
CPU: 2 Intel E5-2670, 8-core, 2.6 GHz
GPU: 2 NVIDIA Tesla K20
RAM: 256 GB / 64 GB
Network interfaces: 2x10 Gb Ethernet, 56 Gbps Infiniband / 56 Gbps Infiniband
Station module:
Input stream decoding
Delay tracking
Phase calibration signal extraction
Data synchronization
Bits repacking
Correlation module:
Bits transformation
Fringe rotation
Auto- and cross-correlation spectra processing
Head module:
Interblock processes control
Results collecting

## Slide 6: High-Performance Computing Cluster
Third International VLBI Technology Workshop 10 - 13 November 2014, Groningen/Dwingeloo, the Netherlands
8 Cache servers, 32 V200F compute modules, appropriate power supply and cooling system forms IAA RAS HPC cluster with total peak performance of 85.5 Tflops
Panasas 75 TB Pan-FS storage solution
Melanox 56 Gbps Infiniband network
Notes: Кол-во серверов, инфинибэнд, СХД. Как все с вместе работает.

## Slide 7: Correlator Topology
Third International VLBI Technology Workshop 10 - 13 November 2014, Groningen/Dwingeloo, the Netherlands

## Slide 8: Station Module
Third International VLBI Technology Workshop 10 - 13 November 2014, Groningen/Dwingeloo, the Netherlands

## Slide 9: Correlation Module
Third International VLBI Technology Workshop 10 - 13 November 2014, Groningen/Dwingeloo, the Netherlands
Cross-correlation algorithm
Cross-correlation is done for all stations and all polarizations including auto-correlation generating 78 spectra for 6 stations 2 polarizations.
9

## Slide 10: Station Module Benchmarking
Third International VLBI Technology Workshop 10 - 13 November 2014, Groningen/Dwingeloo, the Netherlands
Time benchmarking for SM data processing of 1 sec 16 Gbps (8-channel, 2-bit)
Operation | Tesla K20X (Kepler)
Reading & delay tracking | 0.98 s
Buffer repacking | 0.32 s
Pcal repacking | 0.21 s
Pcal reduction | 0.19 s
Performance of station module is enough for accomplishing the required operations

## Slide 11: Correlation Module Benchmarking
Third International VLBI Technology Workshop 10 - 13 November 2014, Groningen/Dwingeloo, the Netherlands
Time benchmarking for 2-station processing of 64 million samples
Operation | Tesla K20X (Kepler)
Bits unpacking and fringe rotation | 23 ms (22 GBps)
FFT | 6.5 ms (154 GBps)
Spectra multiplication | 6.6 ms (150 GBps)
These algorithms require 7 Kepler K20x blades for near-real time processing of one wideband (512 MHz, 2 Gbps) data stream
Notes: Первые два значения для станции, последнее для базы. Первые два знач-я 2х. Последнее 3х для всех вариантов кросс-спетров.

## Slide 12: First Fringe
Third International VLBI Technology Workshop 10 - 13 November 2014, Groningen/Dwingeloo, the Netherlands
Fringe fitting results for the scan of source 1300+580 performed with BRoadband Acquisition System (BRAS) during RUTest-074 series

## Slide 13: First Fringe
Third International VLBI Technology Workshop 10 - 13 November 2014, Groningen/Dwingeloo, the Netherlands
Fringe fitting results for the scan of source 1300+580 performed with BRoadband Acquisition System (BRAS) during RUTest-074 series

## Slide 14: Future Plans
Third International VLBI Technology Workshop 10 - 13 November 2014, Groningen/Dwingeloo, the Netherlands
Late 2014:
Benchmark tests with maximum data rate (6-stations) in IAA RAS
2015:
Final stage of control & GUI software developing and testing
Post-processing system software developing and testing
Regular observations of “Quasar” VLBI network processing

## Slide 15: Thank you!