## Slide 1
Current State of Russian VLBI Broadband Acquisition System
Evgeny Nosov, Anton Berdnikov, Sergey Grenkov, Dmitriy Marshalov, Alexey Melnikov, Leonid Fedotov
Institute of Applied Astronomy
Russian Academy of Sciences

## Slide 2
BRAS structure

## Slide 3
BRAS

## Slide 4
Synchronization module
1 channel of BRAS

## Slide 5
BRAS key features
Number of channels | 8
IF, MHz | 1024-1536
Channel bandwidth, MHz | 512
ADC | 8 bits, Fs=1024 MHz
Output samples width | 2/8 bits
Automatic gain control | For each channel, 32 dB
Sync signals | 5/10/100 MHz (autodetect), 1 PPS x2
Control interface | 10/100 Ethernet
Telemetry | Power circuit currents, temperatures of PCBs and ADCs
Power consumption | 75 W
Size | 19” case, 483x314x242 mm (WxHxD)

## Slide 6
BRAS key features
Data frames format | VDIF
VDIF payload size, bytes | 1000, 1024, 1280, 1600, 2000, … , 8000, 8192
Output interface | 10G Ethernet, X2 transceiver
Output header modes | Ethernet header only, Ethernet + IP Ethernet + IP + UDP
Physical medium | Fiber
Analysis features | Signal power 2-bits data statistics PCAL extraction Both 8 and 2-bits signal capture (1024 samples) Spectrum analysis of captured signal and extracted PCAL (implemented in software) 1PPS int-ext delay monitoring

## Slide 7
BRAS is located in the focal cabin.
Output signals are transmitted to recording system through fiber optical lines in digital form.
Advantages over analog signal transmitted through fiber or coaxial cable:
No influence on frequency response
No EMI induced in IF
Variation of ambient temperature and cable loop bending does not affect the transmitted signal
Reduced amount of equipment (amplifiers, equalizers, RF-to-fiber converters etc.)
BRAS location

## Slide 8
BRAS location in the focal cabin
Chassis
Self-aligning
platform
Main floor

## Slide 9
BRAS chassis in the focal cabin (Badary)

## Slide 10
BRAS vibration and climatic tests

## Slide 11
Test observation 04.09.2014
Baseline: Zc-Bd (Zelenchuk – Badary) on RT-32
Frequency: 8.592-9.104 GHz (512-1024 MHz in IF)
25 sources with flux density from 0.6 to 7.6 Jy and duration from 20 to 127 seconds
Mark5C recording system

## Slide 12
0212+735
1803+784

## Slide 13
PCAL extraction (Zc)
Time, samples
mV

## Slide 14
Phase of PCAL tone (8.805 GHz) vs. time
Time, sec
Phase, deg

## Slide 15
Power spectral density measured by BRAS
dBm/MHz
Frequency, MHz

## Slide 16
100 MHz, fiber
100 MHz, coax.
1024 MHz, fiber
1024 MHz, coax.

## Slide 17
Conclusions
BRAS has been successfully tested on Zelenchukskaya-Badary baseline on RT-32 antennas
Fine response was received for every scan
The embedded signal analysis features allow remote system condition control
The system is ready to be installed on new RT-13 antennas
Final test with BRAS on RT-13 is scheduled for 2015

## Slide 18
THANK YOU FOR YOUR ATTENTION!