## Slide 1: Data Processing Center for Space VLBI Projects Implementation
Shatskaya M, Abramov A., Fedorov N., Kostenko V., Likhachev S., Seliverstov S., Sichev D. Astro Space Center, P. Lebedev Physical Institute, RAS, Moscow, Russia

## Slide 2
Data processing center for space VLBI project Radioastron. Now working project.
Data processing center for space VLBI project Millimetron. Future project.

## Slide 3: Objectives of Data Processing Center
Organization of service information exchange.
Collection and storage of all scientific information of observations.
Processing of scientific observation data.

## Slide 4
 | Expected July 2011 | Nowadays 2014
Ground Telescopes | 5 | 40
Ground Telescopes Worked Simultaneously | 2-3 | Up to 30
Tracking stations | Pushchino | Pushchino + Green Bank
Number of observations per month | 20 | 120
Volume of information, TB per month | 10 | 120

## Slide 6
 | At the launch | Nowadays
Storage | 100 TB | 1 PB on line 2 PB off line
 | DAS Direct Attached Storage | NAS Network Attached Storage
 |  | Dividing of processes of data collecting and archiving and processing
Internet Channel | 100 Mb/s | 600 Mb/s
Internal Network | 1 Gb/s | 10 Gb/s

## Slide 7
Exterior View of Data Processing Center

## Slide 8: Structure of Data Processing Center

## Slide 9
- On-line storage system for collecting information - 600TB;
- On-line storage system for data processing - 80TB;
- On-line storage system for processing results - 120TB;
- The archive of data on hard drives - 2000TB;
- Archive tapes for 2000 TB;
- Reserve storage 20 TB in Pushchino;
The total storage capacity is about 5PB!
- Computer system with performance 1TF/s;
1Gb/s and 10Gbit/c network infrastructure,
and 600 Mbit/s Internet channel.
Main Components of DPC

## Slide 10: Archive on HDD
Total amount of data today is more than 1100TB

## Slide 11
Channels of communication

## Slide 12: Scientific Data Transferring
100 GB – 1 hour
Pushchino tracking station –
1 Gb/s direct channel – immediately after observations
Green Bank tracking station and all ground telescopes – via Internet speed - from 4 to 300Mb/s
On HDD if it is possible
On HDD from Kalyasin and Evpatory
We have suitable situation with almost all telescopes

## Slide 13
Transferring of Imaging Observations
Imaging observations from Bonn and JIVE
One observation 40 TB
We need a few hundreds Mbit/s at least
GEANT
TCP UDP
Direct channel

## Slide 14
Space telescope
Ground telescopes
Tracking station
Control stations
Data processing center
Tracking headquarters
Scientific centers and users
Ballistic center
Center of experiment planning
Data Processing Center of Millimetron Project

## Slide 15: Millimetron: Amount of Expected Information
Maximum from tracking stations:
1,2 Gb/s * 3600s * 24hours * 365days * 5years ~ 23,7 PB
From ground telescopes
2,4 Gb/s * 3600s * 10 hours * 365 days * 5 years ~ 19,2 PB
Total amount from tracking stations and 3 ground telescopes:
23,7 + 19,2 * 3 = 81,3 PB
According to Technical Documentation
5 ПБ on-line = 4 PB for row data + 1 PB after correlator
200 PB archive = 100 PБ the first copy + 100 PБ the second copy

## Slide 16: Data Center for Millimetron Project
Appropriate room or special building with protection from leaking and fire-extinguishing system
Redundant power supply
Independent power supply (diesel generator)
Uninterruptible power supply
Air-conditioning on N + 1 systems
Video surveillance and monitoring of all systems
Room for operators
Communication channels

## Slide 17: Data Center for Millimetron Project
Computer equipment - repositories, supercomputer, archive, communications
Buffer storages on Tracking Stations
1,2 Gb/s * 3600s * 16 hours * 14 days ~120 TB
Buffer storage on ground telescopes
2,4 Gb/s * 3600s * 16 hours * 14 days ~ 240 TB

## Slide 18
The structure and functions of ASC Data Processing Center for Radioastron project are fully adequate to the data processing requirements of the Radioastron Mission.
When we created data processing center for the Radioastron project, we got experience of working, transferring and storage of large volumes of data. The experience will be useful for our next project "Millimetron“.
Conclusions

## Slide 19
THANK YOU

## Slide 20: Scientific Data Transferring from Ground Telescopes
Effelsberg Germany
Arecibo Puerto Rico
GBT USA
Medicina Italy
Westerbork Netherlands
Yebes Spain
Badary Russia
Zelenchuk Russia
Svetloe Russia
Usuda Japan

## Slide 21: Scientific Data Transferring from Ground Telescopes
Urumqi China
Tidbinbilla Australia
Shanghai China
Parks Australia
Onsala Sweden
Noto Italy
Jodrell Bank UK
ATCA Australia
Hart Africa
Robledo Spain
Torun Poland

## Slide 22
Noto Италия
Jodrell Bank
Великобритания
Hart ЮАР
Effelsberg Германия
Arecibo Пуэрто-Рико
GBT США
Medicina Италия
Westerbork
Нидерланды
Yebes Испания
Бадары Россия
Zelenchuk Россия
Svetloe Россия